Avalanche Statistics of Dislocation Plasticity
Rohan Tiwari | The Micromechanical Materials Modelling (MiMM) group | IMFD | TU Bergakademie Freiberg

---
Introduction
What is a Dislocation avalanche?
In macroscopic scale, the plastic deformation appears as smooth curve, but in microscopic scale the deformation happens intermittently i.e.,it takes place through strain bursts. This happens due to dislocation avalanche.
Avalanche starts with dislocation accumulation and formation of dislocation bands. The dislocation gets piled up before the bands whose give away causes avalanches(like opening a flood gate)

---
Self-Organized Criticality:
- Any Slowly driven non-equilibrium systems self-organize themselves in a critical state where anything can happen within well defined statistical laws
- They are Scale-free, intermittent, follows power law distribution and the external driving of the system needs to be much slower than the internal relaxation
- Dislocation avalanches also possess the same character with the power law distribution given by P(A) = A-τ
  where A - Number of bursts
  P(A) - Magnitude of bursts
  τ - 1.6-2.0

---
Measurement of Dislocation avalanches:
- Acoustic emission (AE) is a technique used to measure dislocation avalanches because avalanches generate acoustic waves which can be used to describe its properties
- Ice is used as a model material to study dislocation dynamics from AE because 1) Ice can be easily grown in laboratory 2) Transparency allows to verify AE is not related to micro-cracking 3)Twinning does not occur in ice 4)and AE transducer can be easily coupled by melting/freezing
- One to six piezoelectric transducers of bandwidth 200-750 kHz is attached to the side surface of the cylindrical sample. The dynamic range of the amplitude threshold was set between 30db and 100dB. For each detection above threshold the AE system measures parameters like to , te ,δ and Ao. Acoustic wave form of a dislocation avalanche is shown as follows

---
The wave is recorded is then compared with the acoustic wave having same average duration Ao which provides information about how fast an avalanche damps from initial propagation velocity